## Slide 1
HEATER CONTROLLER
CARRIAGE
LINEAR ACTUATOR
FEED MOTOR CONTROLLER
WIND MOTOR CONTROLLER
PREFORM
ELECTRIC HEATER
FIBER COLLECTOR
DINPUT
DOUTPUT
LSTART
LFINAL
FEED RATE
UPTAKE RATE
SET POINT
ARDUINO
SET POINT
IN-LINE FIBER DIAM DETECTOR
FEEDER TC
HEATER TC 2
HEATER TC 1
UPTAKE TC
Assuming:
Dpreform = 20 mm and Dfiber = 0.2 mm
Reduction of diameter by 100x
=
Increased length by 10,000x
Therefore:
If vfeedrate = 1 mm/s,
Then vuptakerate = 10,000 mm/s
Tensiometer
Pre-shape preforms to have a conical tip?
Thermal Draw Tower Concept:
Cooling Fans

## Slide 2
ATS Temperature Control System
3D Printed CARRIAGE & CLAMP
Velmex X-Slide
(XN-0060-E02-21)
TB6600 Microstep Driver
ATS Series 3210-2.00 8-4 Furnace
FilaBot Filament Winder
DOUTPUT Reader
Furnace Power
PC Software Requirements: Arduino IDE – Create microcontroller code loops
LK-Navigator2 – control Keyence in-line detector
KEYENCE LS-9030MT
FEEDER TC (?)
HEATER TC 2
HEATER TC 1
UPTAKE TC (?)
Checkline Tension Sensor
(TS-2L-500-AL)
TC 2
TC 1
Motor Wiring
Pos and Neg Limit Switches
+24VDC Power Adapter
120V AC Wall Socket
KEYENCE LS-9501P
In-Line Controller
Power Cable
Head Cable
+24VDC Power Adapter
USB Cable
120V AC Wall Socket
120V AC Wall Socket
PC USB PORT 2
Power Cable
120V AC Wall Socket
5kohm/5kohm Voltage Divider
Power Cable
120V AC Wall Socket
Analog Output (+0-10VDC)
Speed Control
Tension Reader
Visual Summary of Thermal Drawing Apparatus Hardware Connections and Software Requirements
Checkline SC-PM Display Unit
5-Wire Cable
Manually Controlled Temperature Setpoint
Analog Output (+/-10VDC)
24V Power Supply
Stepper Motor
Arduino Uno R3
3D Printed Mounts
Enable, Direction, Pulse, GND
Pos Limit
Neg Limit
Pos Limit Read
Pos Limit Write
Neg Limit Read
Neg Limit Write
Analog Output (+0-5VDC)

## Slide 3
Filafab Winder
Speed CTRL
Winder Toggle
Rot Pot 2
Rot Pot 1
Direction Mode Selector
Feed Speed: X.XX mm/min
Tension: YYY grs
Winder Speed: Z.ZZ m/min
Diameter: WWW um
Digi Pot
OLED Display
Enable
Limit Switches
NEMA 23 Motor
+12-24VDC Adapter
TB6600 Stepper Motor Controller
Tensiometer
+0-10V Signal
Voltage Divider
Tensiometer
+0-5V Signal

## Slide 4
FeedMotor StepPin
FeedMotor DirectionPin
+5V
Digital Potentiometer
Tensiometer
FILAWINDER
GND
Rotary Potentiometer
FeedMotor neg_limit_pin WRITE
FeedMotor pos_limit_pin READ
I2C SCL
I2C SDA
DC Power
USB
FeedMotor neg_limit_pin READ
FeedMotor pos_limit_pin WRITE
GND
GND

## Slide 5: Arduino Uno R3 Board Dimensions

## Slide 6: Arduino Uno R3 Electrical Schematic

## Slide 7: Motor Speed Calculation
Velmex X-Slide E02 screw pitch = 0.200” = 5.08 mm per revolution
TB6600 Microstep Driver:
  DIP switches {1-2-3} set to {OFF-OFF-ON} for 3200 steps per revolution
  DIP switches {4-5-6} set to {OFF-OFF-ON} for 2.8A of supply current
5080 um / 3200 steps = 1.6 um / step
Pulse delay rpm_t = 60,000,000 us / 2 pauses / _pulse / _rpm
For pulses = 3200 and RPM = 1, rpm_t = 4,687.5 us/pause

## Slide 8: TB6600 Microstep Driver
Controls a unipolar stepper motor by use of 24V external power supply and microcontroller triggering
Pin connections:
  Ena + : Digital Pin 12
  Dir + : Digital Pin 11
  Pul + : Digital Pin 10
  Ena -, Dir -, Pul - : Digital Ground
  A+/-, B+/- : Motor wires
  GND : Power Supply Ground
  VCC : +24 VDC
6 DIP switches allow selection of various steps/revolution and sets supply current (details on next slide)

## Slide 9
Nema 23 motor current = 2.8A
OFF|OFF|ON|OFF|OFF|ON
3200 steps per revolution

## Slide 10
1 – BLUE – C (GND)
2 – BLACK – NC (INT)
----
3 – WHITE – NC (INT)
4 – GREEN – C (GND)

## Slide 11: AccelStepper.h Library
AccelStepper.feedmotor(AccelStepper::DRIVER (interface), step_pin, dir_pin)
Return the carriage to the top starting point by pressing both switches to enable the software loop, then press the bottom (positive) limit switch to reverse the direction of the run() command and over-ride the user set feed speed with the maximum. This should run until the top (negative) limit switch is triggered, at this point the motor should be stopped, the direction reversed and then moved down a couple full rotations (approx. 5mm per revolution; 3200 steps per revolution)

## Slide 12
Initialize Settings and Display
Update Settings based on user inputs
runSpeed()
updateDisplay()
limitSwitch()
  If BOTH limit switches are being triggered together: user initiating software
  If EITHER limit switch is hit while the OTHER is not: stop motor & reverse direction
  If NEITHER limit switch is being triggered: carriage should run at set speed (user or software)
  While the limit switches are triggered, without some reverse movement, they will stay triggered and never enter the NEITHER condition
Reverse direction()

## Slide 13: SSD1306 OLED Display – I2C
Provides real-time text readouts of process settings such as feed speed, uptake speed, tension, diameter, etc.
Pin connections:
  GND : GND
  VCC : +5 V
  SCL : SCL Comm Bus
  SDA : SDA Comm Bus
SSD1306
OLED Display 128x64
SDA
SCL
+5V
GND

## Slide 14: SSD1306 OLED Display Dimensions

## Slide 15: DS3502 Digital Potentiometer – I2C
Digitally controls analog wiper pin RW from 0 – 5 V
Pin connections:
  RL, GND : GND
  RH, VCC : +5 V
  RW : Analog I/O Pin A0
  SCL : SCL Comm Bus
  SDA : SDA Comm Bus
  V+, A0, A1 : No Connection
DS3502
Digital Potentiometer
SDA
SCL
+5V
GND
SDA
SCL
+5V
GND

## Slide 16: Uptake Motor and Spoolage
Need an uptake motor capable of moving at the necessary RPMs for the effective spooling of drawn fibers
Assuming the final diameter is 100X smaller than the input diameter, the uptake motor should wind at approximately 100X the feed motor
Not sure whether a stepper motor is ideal here or if a DC motor controlled by the digital potentiometer would be better

## Slide 17: Checkline TS2L-500 Tensiometer
0 – 500 g measuring range (too high) probably
Connects by cable to display unit
Pin and Wire Connections:

## Slide 18: Checkline SC-PM Display Unit
Connects to a 24 VDC wall-socket power adapter and the 5-wire cable
Analog Signal Out (+) pin supplies 0 – 10 V
  Use a voltage divider to reduce the signal range to 0 – 5 V so that it is acceptable for Arduino
  Connect to an Analog I/O pin on the Arduino Uno R3
N/A

## Slide 19: Tensiometer Interface

## Slide 20: Keyence In-Line Diameter Measurement
Mounted into position below the furnace to measure the output fiber diameter
  Output diameter could be a quality control metric independent of the restof the system
  Or, the output signal could be used to feed back into the Arduino to adjust the process to increase/decrease uptake/feed rate based on the measured value
Set up a measurement program using the Keyence software (LS-Navigator2), including necessary steps to enable signal collection using the analog outputs *(note: these necessary steps will need to be determined at the time of implementation.)

## Slide 26
BACK FACE
FEED SPEED: WIND SPEED:
DIAMETER: TENSION:
Wind Speed
Feed Speed
On/Off
Wind Ctrl Mode
Feed Dir
o|G|T|3|4|o
Cable Hole
6-pin Connector

## Slide 27
BACK FACE
FEED SPEED: WIND SPEED:
DRAW RATIO:
DIAMETER:
Wind Speed
Feed Speed
On/Off
Wind Ctrl Mode
Feed Dir
o|G|T|3|4|o
Cable Hole
6-pin Connector
Updated Controls, 2024-December-03
L
R
R
L
M
Feed Dir Switch Options:
L:
M: Automatic mode (leave in this position)
R:
Wind Ctrl Mode Options:
L: Winder speed controlled by drive knob on the winder unit itself
R: Winder speed controlled by arduino

## Slide 28: MATERIALS
Low-Density Polyethylene (LDPE)
  Thermoplastic made from ethylene
  C2H4)n
  917-930 kg/m3
  Can handle temps of 65C consistently and 90C briefly
  Less crystalline than HDPE
High-Density Polyethylene (HDPE)
  Thermoplastic made from ethylene
  930-970 kg/m3
Polypropylene (PP)
  Thermoplastic polymer from propylene
  C3H6)n
Polyethylene Terephthalate Glycol (PETG)
Polylactic Acid (PLA)
Styrene-Ethylene-Butylene-Stryrene (SEBS)
  Thermoplastic elastomer

## Slide 29: Low-Density Polyethylene (LDPE)
Density | 0.88 – 0.96 g/cm3
Melting point | 115 – 135°C
Glass Transition Temperature | °C
Temperature of crystallization | °C
Latent heat of fusion | kJ/kg
Thermal conductivity | W/m-K
Specific heat capacity | J/kg-K
Specific heat (solid) | kJ/kg-K
Crystallinity | %

## Slide 30: High-Density Polyethylene (HDPE)
Density | 961 kg/m3
Melting point | 131.8 °C.
Temperature of crystallization | 121.9 °C.
Latent heat of fusion | 188.6 kJ/kg.
Thermal conductivity | 0.54 W/m.°C. at °C.
Specific heat capacity | 1331 to 2400 J/kg-K
Specific heat (solid) | 2.9 kJ/kg. °C.
Crystallinity | 61%

## Slide 31: Polypropylene (PP)
Density | 0.855 g/cm3 (amorphous) 0.946 g/cm3 (crystalline)
Melting point | 130 – 171°C
Glass Transition Temperature | -10°C (amorphous, atactic) -8°C (semi-crystalline, syndiotactic) 0°C (semi-crystalline, isostatic)
Temperature of crystallization | °C
Latent heat of fusion | kJ/kg
Thermal conductivity | W/m-K
Specific heat capacity | J/kg-K
Specific heat (solid) | kJ/kg-K
Crystallinity | %
Notes: https://en.wikipedia.org/wiki/Polypropylene

## Slide 32: Polylactic Acid (PLA)
Density | kg/m3
Melting point | °C
Glass Transition Temperature | °C
Temperature of crystallization | °C
Latent heat of fusion | kJ/kg
Thermal conductivity | W/m-K
Specific heat capacity | J/kg-K
Specific heat (solid) | kJ/kg-K
Crystallinity | %

## Slide 33: Polyethylene Terephthalate Glycol (PETG)
Density | kg/m3
Melting point | °C
Glass Transition Temperature | °C
Temperature of crystallization | °C
Latent heat of fusion | kJ/kg
Thermal conductivity | W/m-K
Specific heat capacity | J/kg-K
Specific heat (solid) | kJ/kg-K
Crystallinity | %

## Slide 34: Styrene-Ethylene-Butylene-Styrene (SEBS)
Density | kg/m3
Melting point | °C
Glass Transition Temperature | °C
Temperature of crystallization | °C
Latent heat of fusion | kJ/kg
Thermal conductivity | W/m-K
Specific heat capacity | J/kg-K
Specific heat (solid) | kJ/kg-K
Crystallinity | %

## Slide 35: ATS Furnace Temperature Controller
Current temperature
Adjust target
Target temperature
Power On
Power On
(Safety)